## Slide 1: Breath of Life: Tricks to Master Mechanical Ventilation
Nicholas Spartan Santavicca, MD
Emergency Medicine, Internal Medicine, Critical Care
Montefiore Medical Center

## Slide 2: Goals of Mechanical Ventilation
Goals of Oxygenation (PEEP, FiO2)
  SpO2 88 – 95%
  PaO2 55 – 80mmHg
  FiO2 < 60%
  Goals of Ventilation (TV, RR)
  6 – 8cc/kg IBW
  pH ~ 7.25 – 7.3
  Goals of Mechanics
  Driving pressure (DP) < 14cm H2O
  Pplat < 30cm H20
  PIP < 40cm H2O if possible
  Synchronous flow loops
Notes: Talk about titrate oxygenation via PEEP and FiO2.
Ventilation via TV and RR.

## Slide 3: Remember…
PIP, Pplat relationship
  PIP > Pplat  think obstruction, increased resistance
  PIP ≈ Pplat  think worsening compliance, stiffer lungs
Look at wave forms
  Exhalation curve should return to baseline
  Inhalation pressures should be linear or flat

## Slide 4: Case 1
42yo F p/w 3 days of worsening cough and SOB
RR 38 and 82% on RA
On HFNC, RR 32, 88% and increased WOB

## Slide 5: Case 2
63 yo M hx COPD on 3L home O2 p/w worsening shortness of breath
Drowsy, RR 34, no air movement throughout
ABG 7.12 / >100 / 75
Tried on BiPAP for 30 min without improvement

## Slide 6: Case 3
73yo M hx COPD p/w shortness of breath after running out of meds x 2 weeks
RR 30, O2 sat 88% on 2L
Diminished breath sounds throughout
7.32 / 87 / 69
Do Not Intubate
Notes: ACUTE: every 10 increase in CO2, pH drops 0.08 or HCO3 increases by 1
CHRONIC: every 10 increase in CO2, pH drops 0.03 and HCO3 increases by 3.

## Slide 7
> 85% had < 5 hours education in past year
90% > 1 intubated patient / month
  60% > 4 patients / month
>40% do not feel comfortable
>75% by RT
Notes: Surveyed residents regarding training and comfort with mechanical ventilation.
Primarily surveyed North eastern US – 312 EM residents.

## Slide 8: Respiratory Failure
Type 1 (hypoxic)
  V/Q mismatch
  Low barometric pressure (Mt. Everest)
  Low FiO2 (Scuba diving, space)
  Diffusion impairment (ILD, IPF)
  Alveolar hypoventilation (Baltimore)
Shunt
Dead Space

## Slide 9: Respiratory Failure
Type 2 (hypercapnic)
  Hypoventilation (Baltimore)
  Increased dead space
  Increased CO2 production
Type 3 (mixed)

## Slide 10: Positive Pressure Ventilation
What it does?
  Decreases WOB
  Restores gas exchange
Notes: We have to remember to treatment for respiratory failure is positive pressure ventilation (both invasive, noninvasive).
They do this, in broad strokes by decreasing WOB and restoring gas exchange by recruiting better lung and improving mechanics.
There are, just like any treatment in medicine, some downsides and risks involved.
As you push air into the lungs, completely flip pressure gradients from normal physiology (spontaneous breathing is negative pressure system)
- By breathing via positive pressure, you decrease venous return (in preload dependent states (RV failure – submassive/massive PE, tamponade, RV failure/pHTN exacerbation.

## Slide 11: Positive Pressure Ventilation
Risks
  Preload dependent states
    Under-resuscitated
    RV failure
      PE, pHTN exacerbation, MI
    Tamponade
  Thoracic compartment syndrome
  Lung damage
Notes: There are, just like any treatment in medicine, some downsides and risks involved.
As you push air into the lungs, completely flip pressure gradients from normal physiology (spontaneous breathing is negative pressure system)
- By breathing via positive pressure, you decrease venous return (in preload dependent states (RV failure – submassive/massive PE, tamponade, RV failure/pHTN exacerbation.

## Slide 12: Compliance
Compliance =
  V  P = decreased compliance
  V  P = increased compliance
ARDS
COPD
Notes: Think of this as the EF of the lung

## Slide 13: Inspiration
Trigger (initiates inspiration)
  Patient effort – Assisted breath
  Machine effort – Controlled breath
Target (cannot be exceeded)
  Set flow
  Set inspiratory pressure
Cycle (terminates inspiration)
  Set volume
  Set inspiratory time
Notes: Inspiration is what we control during mechanical ventilation. We control the time and amount of pressures/flows involved during expiration.

## Slide 14: Expiration
Purely passive
Based on
  Expiratory time
  Obstruction
Can adjust based on flow and RR

## Slide 15: Example of respiratory phases
RR 15 BPM
Respiratory cycle = insp + expiratory times
  60/15 = 4s
Ins time (we set) – usually 0.8 to 1.2s
  i.e. 1s
Expiration = resp cycle – insp
  4s – 1s = 3s

## Slide 16: Types of breathing
Pressure cycled modes – fixed pressure at variable volumes
  CPAP
  BiPAP
  Pressure Support
  Assist Control (PCAC)
Volume cycled modes – fixed volume at variable pressures
  Assist Control (VCAC)
  Intermittent Mandatory Ventilation (IMV)
  Synchronous Intermittent Mandatory Ventilation (SIMV)
Pressure Regulated Volume Control

## Slide 17: Volume control
We set:
  Tidal Volume, iflow
  RR
  PEEP
  FiO2
  I:E (indirectly)
We evaluate:
  PIP
  Pplat
  MV
Notes: Important when need to ensure ventilation.
Constant flow  over certain designated time.
Rise in pressure to overcome ETT and proximal airways  then see rise in pressure in linear fashion as lungs become inflated (related to compliance of lungs). Then at end of breath, if perform inspiratory hold, resistance pressure (prox airways/ETT) becomes 0 and pressure is reflected as Pplat.

## Slide 18: Pressure Control
We set:
  PIP
  PEEP
  RR, Inspiratory time
  FiO2
We evaluate:
  TV
  I:E ratio
Notes: Need to be cautious when compliance is changing.

## Slide 19: PC vs. VC
 | Pressure Control | Volume Control
Tidal Volume | Variable | We set
PIP | We set | Variable
Pplat | We set | Variable
Flow | Variable | We set
Flow pattern | Decelerating | We set

## Slide 20: PRVC
Uses minimal pressure to achieve set volume
  Adapts, varies pressures due to changing compliance
Tries to adapt to changing resistance, compliance
  More comfortable
Decelerating flow pattern
  Can receive high inspiratory flows
Harmful when agitated, dyssynchrony
  Thinks patient doing more work
Notes: Set your target TV and maximum Pressure.

## Slide 21: Case 1
42yo F p/w 3 days of worsening cough and SOB
RR 38 and 82% on RA
Intubated with 6.0 ETT
ABG 7.32 / 48 / 156 on 100 % FiO2
Notes: Want to go back to case 1 – clearly a hypoxic (T1 ) respiratory failure.
So we decide to intubate him. We see there is an 6.0 ETT tube. When we ask why, they say it is what we have.
According to Berlin criterial, moderate ARDS

## Slide 22
Notes: ARDS is not good lung, bad lung but a spectrum of diseased lung. Think of it like stroke and brain. You have diseased lung completely not participating in gas exchange and a small amount of good lung totally efficient and a good proportion acting like the prenumbra that could be salvageable. To do this we need to limit Ventilator induced lung injury and not shoot ourselves in the foot.
By following these goals, limit ventilator-induced lung injury

## Slide 23: Goals of Mechanical Ventilation
Goals of Oxygenation
  SpO2 88 – 95%
  PaO2 55 – 80mmHg
  FiO2 < 60%
  Goals of Ventilation
  6 – 8cc/kg IBW
  pH 7.25 – 7.3
  Goals of Mechanics
  Driving pressure (DP) < 14cm H2O
  Pplat < 30cm H20
  PIP < 40cm H2O if possible
  Synchronous flow loops
Notes: You want to keep in mind when dealing with ARDS because these parameters limit VILI.

## Slide 24
Notes: Volutrauma – overdistension – as with high TV ventilation
Barotrauma – high peak pressures
Atelectrauma – opening and closing of alveoli
Biotrauma – caused by dyssynchrony
Oxygen toxicity – theoretical from 60% is ok, but known that excess O2 is harmful.

## Slide 25
Atelectotrauma
Barotrauma
Volutrauma
Notes: Pressure volume loops of alveoli. Think of this as the Frank Starling curve of the lung.

## Slide 26: Case 1
PRVC 400 / 15 / 5 / 40
Called to room due to vent alarm
PIP continued to be 45
What else do you want to know?
  Pplat is 26
What does this mean?
45

## Slide 27: PIP > Pplat
ΔP = Driving pressure = Pplat – PEEP
ΔP = (Flow x resistance) + (TV/Compliance)
Resistance pressure
Elastic pressure
ETT, proximal airways
Notes: Flow x resistance is dynamic component of breath (based on resistance of airways)
Tv, compliance is representative of the state of the lung parenchyma.

## Slide 28: Peak > Plateau
 resistance
ΔP = (Flow x resistance) + (TV/Compliance)
ΔP = (Flow x resistance)
Poiseuille’s Law
Notes: Why do we care about this stuff?

## Slide 29: PIP > Pplat
Size of ETT
  Consider tube exchange
Obstruction (mucus plug, biting tube, kink)
  Suction
  Bronchoscopy?
  Increase PEEP – blowout
  Pull the tube!?
Bronchospasm
  bronchodilators

## Slide 30: Case 1
Exchange tube to 8.0 ETT
1hr later, called into room due vent alarm again
What else you want to know?
  Pplat 35
What does this mean?
38

## Slide 31: Peak ≈ Plateau
 PIP ≈ Pplat ( compliance)
P = (Flow x resistance) + (TV / Compliance)
ΔP = (TV / Compliance)
Notes: Why do we care about this stuff. Because

## Slide 32: Peak and Plateau
PIP ~ Pplat
  ARDS, ALI
    Consider adjuvant treatments
  Pulmonary edema
  Pneumothorax
    Get your US, XR
  Atelectasis
    Recruitment maneuver, consider bronchoscopy
  Restrictive lung disease disease
  Auto-PEEP
Notes: Need amnemonic  AARPx3
ARDS, Atelectasis, Restrictive lung Dz, pulm edema, Ptx, PEEP

## Slide 33: Case 2
63 yo M hx COPD on 3L home O2 p/w worsening shortness of breath
Intubated
VCAC 450 / 30 / 5 / 60
Called to room for hypotension
38
5

## Slide 34: Air trapping, Auto PEEP
Buildup of residual volume
  Intrinsic physiology (COPD, bronchospasm)
  Short expiratory times
  Double triggering, dyssynchony
     intrathoracic pressure  thoracic compartment syndrome

## Slide 35: Combating Auto PEEP
Perform end inspiratory hold
Treatment:
  Shortening Insp Time (inc flow)
  Lengthening Exp Time (decrease RR)
  Bronchodilators
  Sedation, pain?

## Slide 36: Case 2
45 minutes later, called back to room
Patient increasing WOB
Dyssynchronous

## Slide 37: Scalloping, sucking down
Seen in volume control
Patient wants
  Higher flow
  Higher volumes
Increased WOB
Treat by:
  Increasing flow
  Increasing TV
  Switch to PC

## Slide 38: Treat scalloping, suck down
Treat by:
  Increasing flow
  Increasing TV
  Switch to PC

## Slide 39: Remember…
PIP, Pplat relationship
  PIP > Pplat  think obstruction, increased resistance
  PIP ≈ Pplat  think worsening compliance, stiffer lungs
Look at wave forms
  Exhalation curve should return to baseline
  Inhalation pressures should be linear or flat

## Slide 40: Goals of Mechanical Ventilation
Goals of Oxygenation
  SpO2 88 – 95%
  PaO2 55 – 80mmHg
  FiO2 < 60%
  Goals of Ventilation
  6 – 8cc/kg IBW
  pH ~ 7.25 – 7.3
  Goals of Mechanics
  Driving pressure (DP) < 14cm H2O
  Pplat < 30cm H20
  PIP < 40cm H2O if possible
  Synchronous flow loops

## Slide 41: Thank You!!!
Questions?????